## Slide 1
Importance of Road Infrastructure Safety Management
Julius Uhlmann - Bauhaus Universität Weimar / Tomasz Mackun - Gdańsk University of Technology
Summer School Zagreb 2026

## Slide 4
WHAT DOES IT MEAN TO MANAGE SOMETHING ?

## Slide 5: MANAGE SOMETHING ?
ANALYSIS
IDENTIFICATION
PLAN
ACTION
Risk ASSESSMENT
DATABASE
EVALUATION
DATABASE OF ROAD ACCIDENTS
CONFLICTS ANALYSIS
INSPECTION / AUDIT
LOCAL ANALYSIS

## Slide 6
IS ROAD SAFETY A PROBLEM ?

## Slide 7
Source: World Health Organisation

## Slide 10
2 996 PEOPLE KILLED
DO YOU REMEMBER?

## Slide 11
What were the consequences of the attack ?

## Slide 13: VICTIMS
Iraq `` 22 000 - 655 000 depends on source
USA and Alliances About 4 000 people killed

## Slide 14: SO WHY WE START A WAR FOR 3000 VICTIMS AND AT THE SAME TIME DO SO LITTLE WHEN OVER 1.3 MILLION PEOPLE GET KILLED ON THE ROAD ?
WHAT DO YOU THINK NOW ?
IS ROAD SAFETY A PROBLEM ?

## Slide 15
Source: World Health Organisation

## Slide 16
Source: World Health Organisation

## Slide 17
Source: World Health Organisation

## Slide 18: Differences between the countries
Source: European Comission
EU
IT
DE
PL
SE
HR

## Slide 19
Factors influencing traffic safety
Notes: We are focussing on Infrastructure, because that is our background. The other two domains are equally important.

## Slide 20
Factors influencing traffic safety
Notes: We are focussing on Infrastructure, because that is our background. The other two domains are equally important.

## Slide 21
Darkness
Notes: Example: A car drives on a road, it is dark

## Slide 22
Darkness
Rain
Notes: It starts to rain

## Slide 23
Darkness
Rain
Small curve radius
Notes: The road has small radius

## Slide 24
Darkness
Rain
Small curve radius
Poor pavement quality
Notes: The quality of the pavement is poor

## Slide 25
Darkness
Rain
Small curve radius
Poor pavement quality
Distraction
Notes: The driver is distracted – CRASH

## Slide 26
Darkness
Rain
Small curve radius
Poor pavement quality
Distraction
Crash
Notes: The driver is distracted – CRASH

## Slide 27: Factors influencing traffic safety
Darkness
Rain
Small curve radius
Poor pavement quality
Distraction
Threshold
Notes: On a good road in good condtions, the distraction might not have been enough to cause an accident, but in the sum of factors it did, as it surpassed a threshold.

## Slide 28: Factors influencing traffic safety
Darkness
Rain
Small curve radius
Poor pavement quality
Distraction
Threshold
Notes: Road Infrastrcture Safety Management can mitigate that. If the pavement would have been better, the accident might have been preventable.

## Slide 29: Safe System Approach
Source: National Safety Council
Notes: In an extension, there can be more factors included in a safe system approach, such as the post crash care

## Slide 30: Safe System Approach
Source: Lars Ekman, Trafikverket
Notes: Swedish safe system Approach:
There are only certain sppeds up to which a crash is survivable. So adjust the speed limits to reduce fatalities or prevent those accidents, e.g. with a median (first example).

## Slide 31: How can we influence infrastructure safety?
Good design standards
Good planning
Good building quality
Good maintainance
Good management
Notes: Good management of the whole process

## Slide 32
EXERCISE
Undivided rural
Regional road sections
Poland

## Slide 33
Risk calculations
20 minutes
Undivided rural
Regional road sections
Poland

## Slide 34: Risk calculations
Select road safety management methods that could solve the problem – to find the most dengerous regional road section
Road | Section | FROM | TO | Length | AADT | Accident | Fatalities | Seriously injured | Light injuries | Ped. Crossings | Schools | Speed limit
RR211 | A | 0 | 1550 | 1.55 | 14000 | 8 | 0 | 3 | 12 | 1 | No | 90
RR211 | B | 1550 | 3640 | 2.09 | 13000 | 2 | 1 | 1 | 2 | 4 | Yes | 50
RR211 | C | 3640 | 5570 | 1.93 | 7500 | 0 | 0 | 0 | 0 | 3 | Yes | 70
RR211 | D | 5570 | 8250 | 2.68 | 4000 | 3 | 0 | 2 | 4 | 2 | No | 50
RR211 | E | 8250 | 10030 | 1.78 | 12500 | 6 | 2 | 4 | 6 | 0 | No | 100
RR211 | F | 10030 | 12750 | 2.72 | 9000 | 4 | 0 | 0 | 8 | 5 | Yes | 50
RR211 | G | 12750 | 15300 | 2.55 | 17500 | 5 | 1 | 5 | 10 | 0 | No | 90

## Slide 35
1…..
2…..
Indicate the order in which interventions should be implemented. Select the top three priority sections.
3…..

## Slide 36: EXERCISE
Three approaches to prioritising road safety interventions

## Slide 37: Approach 1: Key Points
Objective: identify sections with the highest number of crashes.
Advantages: simple, transparent, easy to communicate.
Limitation: ignores severity, exposure and vulnerable road users.
Discussion: Should many minor crashes outweigh one fatal crash?

## Slide 38: Approach 1: Crash Frequency
Rank | Section | Crashes
1 | A | 8
2 | E | 6
3 | G | 5
4 | F | 4
5 | D | 3
6 | B | 2
7 | C | 0

## Slide 39: Approach 2: Key Points
Objective: reduce fatalities and serious injuries.
Aligned with Safe System and Vision Zero principles.
Focuses on societal harm rather than crash counts.
Discussion: Should one fatal crash outweigh ten minor injury crashes?

## Slide 40: Approach 2: Crash Severity (Vision Zero)
Rank | Section | Reason
1 | E | 2 fatalities + 4 serious injuries
2 | G | 1 fatality + 5 serious injuries
3 | B | 1 fatality near school
4 | D | 2 serious injuries
5 | A | 3 serious injuries
6 | F | No severe injuries
7 | C | No crashes

## Slide 41: Approach 3: Combines factores
Combines crash frequency, severity and exposure.
Considers AADT, speed, pedestrian crossings and schools.
Supports proactive safety management.
Example ranking: E, B, G, F, A, D, C.

## Slide 42: Comparison of Rankings
Method | Top Priorities
Crash Frequency | A, E, G
Crash Severity | E, G, B
Combines factores | E, B, G

## Slide 43: Key Takeaway
There is no single correct ranking.
Different objectives lead to different priorities.
Data alone do not determine decisions.
The methodology determines the ranking.

## Slide 44: How can we achive good management?
RISM =
  Road Infrastructure – Scope
  Safety – Prevention of negative effects
  Management – A conceptual approach to steering differnt activities

## Slide 45: EU Directives on Road Infrastructure Safety Management

## Slide 46: RISM Levels
Planning
Road Safety Impact Assessment
Design
Road Safety Audit
Operation
Road Safety Inspection
Monitoring
Network-wide Road Safety Assessment
Notes: The four parts of RISM according to the directive

## Slide 47
Notes: The four parts of RISM according to the directive

## Slide 48: Road Safety Impact Assessment
Purpose:
  Compare different implementation scenarios from road safety point of view
When:
  Generally undertaken at planning stage and before a major upgrading of the infrastructure
Scope:
  Part of the road network potentially influenced by a measure
Example (Germany):
  Handbuch für Verkehrssicherheit
Source: International Transport Forum

## Slide 50: Road Safety Audit
Purpose:
  Identify infrastructure or traffic related factors increasing injury or accident risk
When:
  Undertaken during planning, design, construction, pre-opening and early operation stages
Scope:
  A designed road infrastructure
Example (Germany):
  Richtlinie für das Sicherheitsaudit von Straßen (RSAS)
Source: International Transport Forum

## Slide 52: Sokratesa street
Potentially high speed,
Excessively long pedestrian crossing,
Pedestrians have to cross two lanes in one direction.
There is a risk that one vehicle may stop while the other continues moving, with limited visibility of the pedestrian.
Risk of hitting a pedestrian and risk of severe consequences of the incident,
Risk assessment: 1

## Slide 53: Woronicza street
The pedestrian crossing is exceptionally long: 13.0 m, four lanes.
The long straight section encourages drivers to reach high speeds.
Drivers do not slow down in the area of the pedestrian crossing.
Pedestrians either hesitate or run across the crossing.
The situation is unacceptable and may lead to crashes. The observed speed is significantly higher than 50 km/h, which means that a collision at this location would likely result in a seriously injured or fatal casualty.
Risk rating: 0

## Slide 54: Road Safety Inspection
Purpose:
  Identify infrastructure or traffic related factors increasing injury or accident risk
When:
  Generally undertaken during normal operation of a road and may also contribute to error correction and hazard elimination
Scope:
  Part or the entire urban, rural and/or motorway network
Example (Germany):
  Not that clearly implemented – maybe Verkehrsschau
Source: International Transport Forum

## Slide 60: Network-wide Road Safety Assessment
Purpose:
  Identify parts of the network with a high likelihood of crashes
When:
  During the operation of the road network, every few years
Scope:
  Entirety of the road network
Example (Germany):
  Empfehlungen für die Sicherheitsanalyse von Straßennetzen (ESN)

## Slide 64: Sources
https://www.who.int/news-room/fact-sheets/detail/road-traffic-injuries
https://transport.ec.europa.eu/background/road-safety-statistics-2024_en
https://www.ictct.net/wp-content/uploads/32-Warsaw-2019/32-Ekman-presentation.pdf
https://www.nsc.org/speeches-testimony/building-safer-roads-for-all
https://www.itf-oecd.org/sites/default/files/docs/15irtadsafetymanagement.pdf